## Slide 1: Chapter 5. PCR polymerase chain reaction
PART 4: A couple of approaches to help avoid artifacts
First use good lab practice: reactions on ice at all times, careful pipetting to avoid cross contamination etc.

## Slide 2: Determining the best annealing temperature
AIM:
  We want a good amount of product and no artifact bands
APPROACH:
  Use a gradient PCR machine to run multiple replicates of identical PCR reactions, each with a different annealing temperature

## Slide 3: Procedure
Prepare one large reaction and divide into several PCR tubes
Load onto machine with programmed gradient
Identify most effective annealing temp
by gel electrophoresis
500C
600C

## Slide 4: Example, gradient PCR results
52oC  72oC annealing temperature
Higher annealing temperatures result in reduced low-molecular non-specific
amplification and increased amplification of the target amplicon
specific amplicon
Unspecific amplicon
From Takara Inc

## Slide 5: Another approach to avoiding artifacts
We program the PCR machine to start with an annealing temperature that is too high, and then decrease a degree every cycle
So if for instance, the annealing temperature was 55oC, we might start at 66oC
The next cycle the annealing temperature is 65oC
Do this for about 10-12 cycles, and then do 20 more cycles at the final annealing temperature
Because you start higher than the optimal temperature there is no opportunity for artifacts to be generated
Called touchdown PCR

## Slide 6: Finally
Sometimes you cannot avoid artifacts
In that case you can gel purify the band
Run out all of the PCR reaction in a gel using a low percentage, 0.7 or 0.8%
Cut out the agarose that contains the desired band, trimming away excess agarose
Several protocols for purifying the DNA from the band

## Slide 7: Methods
Very old method:
  We used to put the gel band in a pipette tip that had been stuffed with siliconize glass wool and put it in the centrifuge
  The DNA came out in the collection tube underneath, was extracted and precipitated
Low melt agarose:
  You can use agarose that can be heated; the agarose melts and then you do phenol/chloroform extraction, ethanol precipitation
Agarase:
  Instead of melting the agarose, you treat with agarase to degrade it and then you do phenol/chloroform extraction, ethanol precipitation
Collection kits using columns:
  These dissolve the agarose and then the whole solution is poured into a column, and the rest of the procedure is just like other DNA column preps